## Slide 1: Physics Laboratory 2 – Experiment 6a: Heating pump
Lukas Prader1,Andrija Đokić2, Kemal Önen3
Advisor: Dr. Fabio Zappa
Date of experimental execution: 04.05.2023
Date of presentation: xx.05.2023
1 lukas.prader@student.uibk.ac.at
2 andrija.djokic@student.uibk.ac.at
3 kemal.oenen@student.uibk.ac.at

## Slide 2: Overview
Everyday use: Fridge, Air conditioner, heat pump for heating
Source: https://www.snuggenergy.com/blog/heat-pumps-the-snugg-energy-2023-guide

## Slide 3: Overview
Everyday use: Fridge, Air conditioner, heat pump for heating
Very efficient, they practically “steal” the heat of the other medium
Therefore high efficiency quotient
  Relationship between used and output energies
  Normally around 4, at best around 6
  Means with 1kW electricity we get 4kW heat
Source: https://www.rateitgreen.com/green-building-articles/heat-pumps-energy-efficient-and-cost-effective-heating-cooling-solutions/133

## Slide 4: Theoretical background
4 most important laws of thermodynamics
  0. Law: Concept of temperature
  1. Law: Inner energy in connection with work/warmth
  2. Law: Natural warmth transport from objects with higher temperatures to those with smaller → concept of entropy
  3. Law: Absolute zero temperature is outside reach

## Slide 5: Theory – Entropy and Enthalpy
Concept of entropy S
  Logarithmical mass of the statistical weight for most probable macrostate of the system
  Dependent of volume and inner energy ↔ definitions of all thermodynamical sizes
  Stays same for reversible processes, increases for irreversible ones
Concept of enthalpy H
  Easier to follow and manipulate with
  Contains information of relevant inner energy and energy needed for a certain volume under a given pressure
  Chemical reactions, Phase transitions: ∆H is absorbed/emitted energy

## Slide 6: Theory – Phase transitions
Nowadays nearly all heat pumps use transition between gas and fluid
Why? → Great energy in phase transitions
  Example: Water with c=2260kJ/kg, Freon R134a: c=200kJ/kg
Image source: https://www.iea.org/reports/the-future-of-heat-pumps/how-a-heat-pump-works

## Slide 7: Theory – Carnot cyclus
Isentropic compression (1→2): Freon heats up to T of warm reservoir
Isothermic warmth emission (2→3): degradation of Entropy of Freon
Isentropic expansion (3→4): Freon cools down to T of cold reservoir
Isothermic warmth absorption (4→1): increase of Entropy of Freon
Image source: Skriptum GP2-V06a_Waermepumpe

## Slide 8: Theory – Carnot cyclus cont.
Entropy differences of (2→3) and (4→1) are identical
  Therefore: =
  Togetger with 1. law → constant energy of the system: ∆U=Qk+Qh+W=0
Thus we get a coefficient of performance (COP)
  єc= = = = = for heating
  є'c= for cooling

## Slide 9: Theory – Clausius-Rankine cyclus
Isentrophic compression (1→2): idealy all work to enthalpie
Isobaric warmth emission (2→3): Freon heats up the warm reservoir
Isenthalpic expansion (3→4): through throttle valve
Isobaric warmth absorption (4→1): Freon takes warmth from cold res.

## Slide 10: Theory – Clausius-Rankine cyclus cont.
Coefficient of performance:
  єCR=

## Slide 11: Motivation
Goals:

## Slide 12: Experimental setup

## Slide 13: Results

## Slide 14: Plot of energies
Absolute values of cooling, thus a positive incline
Values fitted with a polynomial of 2nd Grade
From there we can approximate the COP at certain points